## Slide 1: CS 494/594: Internetworking Protocols
Nirupama Bulusu
Fall 2021
Notes: These are presenter notes.

## Slide 2: Today
Introduction and class logistics
What is this class about?
Lecture 1

## Slide 3: First things first
Class website is on D2L.
  Please verify that you are able to access the class website.
  Materials organized by Week.
  Please review and comply with “Classroom Requirements for All Students and Faculty Due to Covid-19”.
Discussion Channel on Slack.
  #cs494p594-fall2021
  Invites sent to all students.
Lecture 1

## Slide 4: Instructor: Nirupama Bulusu
Instructor: Nirupama Bulusu
  PhD., Computer Science from UCLA in 2002
  At PSU since 2004
  Networking researcher since 1997, interests:
  “Internet of Things”, Blockchain, Wireless Sensor Networks, Mobile Health, Internet Markets
  Office Hours: Mondays 12:00-1:00 pm on Zoom
    Access via D2L. Set up alternate appointments by email nbulusu@pdx.edu
Lecture 1

## Slide 5: Class Workload
1 project
        assigned Week 2; due 12/3/2021, start early!
5 homework assignments
5 online quizzes
  multiple-choice, multiple attempts permitted
Paper reviews with each homework (for 594 students)
Exams:
  Midterm: 11/1/2021, REMOTE SUBMISSION
  Final: 12/8/2021, REMOTE SUBMISSION
Lecture 1

## Slide 6: Grading
 | 494 | 594
Online Quizzes (5) | 20 | 15
Homework | 20 | 15
Reviews |  | 20
Midterm | 20 | 15
Final Exam | 20 | 15
Project | 20 | 20
Total | 100 | 100
Lecture 1

## Slide 7: This Course
How does the Internet work?
Why does the Internet work?
Lecture 1

## Slide 8: What is the Internet?
Lecture 1

## Slide 9: Broadcast vs. Switched Networks
Communication Networks can be classified based on the way nodes exchange information
  Broadcast
    Information transmitted by one node is received by every other node in the network
    This is very hard to scale to many nodes
    eg. WiFi (Wireless LAN)
Lecture 1

## Slide 10: Broadcast vs. Switched Networks
Communication Networks can be classified based on the way nodes exchange information
  Broadcast
    Information transmitted by one node is received by every other node in the network
    This is very hard to scale to many nodes
  Switched
    Links are point-to-point
    Nodes may be connected via “switches” (this allows sharing of the network)
    Challenge is to figure out how to “route” information from one node to another
    Challenge is how to share the network
Lecture 1

## Slide 11: Communication Networks
Can be classified based on the way nodes exchange information
  Switched
    Circuit Switched (Telephone Network)
    Packet Switched (Internet)
  Broadcast
    Wireless LAN
Lecture 1

## Slide 12: What’s the Internet: “nuts and bolts” view
Lecture 1
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop

## Slide 13
Lecture 1
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What’s the Internet: “nuts and bolts” view
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 14: A closer look at network structure:
Lecture 1
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 15: The network core
Lecture 1
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity

## Slide 16: Packet-switching: store-and-forward
Lecture 1
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
source
R bps
destination
1
2
3
L bits
per packet
R bps
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 17: Packet Switching: queueing delay, loss
Lecture 1
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up

## Slide 18: Two key network-core functions
Lecture 1
forwarding: move packets from router’s input to appropriate router output
routing: determines source-destination route taken by packets
  routing algorithms
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
dest address in arriving
packet’s header

## Slide 19: Alternative core: circuit switching
Lecture 1
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed) performance
circuit segment idle if not used by call (no sharing)
Commonly used in traditional telephone networks

## Slide 20: Some defining Internet characteristics
Federated: The Internet connects different networks
  Interoperability is a key goal
Lecture 1

## Slide 21: Internet structure: network of networks
Question: given millions of access ISPs, how to connect them together?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Lecture 1

## Slide 22: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
Lecture 1

## Slide 23: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
global ISP
Lecture 1

## Slide 24: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
ISP B
ISP A
ISP C
Lecture 1

## Slide 25: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors …. which must be interconnected
ISP B
ISP A
ISP C
IXP
IXP
peering link
Internet exchange point
Lecture 1

## Slide 26: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
regional net
Lecture 1

## Slide 27: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
regional net
Content provider network
Lecture 1

## Slide 28: Internet structure: network of networks
Lecture 1
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
IXP

## Slide 29: Tier-1 ISP: e.g., Sprint
Lecture 1
…
to/from customers
peering
to/from backbone
…
…
…
…
POP: point-of-presence

## Slide 30: Mammoth Scale
> 2.4 Billion Users
> 1 Trillion Unique URLs
> 300 Billion emails sent per day
> 1 Billion Smartphones
> 1 Billion Facebook Users
> 2 Billion Youtube Videos Watched Per Day
Routers that switch 100 Tbps
Links that carry 100 Gbps

## Slide 31: Enormous Heterogeneity
Latency: microseconds to seconds (106)
Queuing Delay: 0 to seconds
Packet loss: 0-90%
End-systems: sensors, cellphones, pacemakers, datacenters, supercomputers
Technology: optical, wireless, satellite, copper
Applications: 40 bytes to 5 GB data transfers; live TV - backup; critical services to entertainment
Users: “governing, governed, operators, malicious, naive, embarrassed, paranoid, addicted, cheap” (Sylvia Ratnasamy)

## Slide 32: Constant Evolution
1970s
  56 kbps “backbone” links
  < 100 computers, a handful of sites in the US
  Killer apps: Telnet and file transfer
Now
  100+ Gbps backbone links
  5 B+ devices, all over the globe
  Countless apps; 20 M Facebook apps installed per day

## Slide 33: Some defining Internet characteristics
Federated: The Internet connects different networks
  Interoperability is a key goal
Mammoth Scale
Enormous heterogeneity and dynamic range
Constant Evolution
Prone to Failure
Lecture 1

## Slide 34: So, why does the Internet work?
Lecture 1
Notes: Having explored some of the defining characteristics of the Internet, we can now explore the question why does the Internet work?
Many aspects of human life — work, school, shopping, live music, government services, chats with friends, calls to aging parents — have moved online in this era of social distancing, all without breaking the network. We have experienced some nits, but the Internet has managed shifts and surges in network usage, but not failed.

## Slide 35: Internet Architecture
Lecture 1
http://www.nap.edu/html/coming_of_age/
http://www.ietf.org/rfc/rfc1958.txt
Notes: The reason for this success lies in some of the design decisions at the inception of the Internet. What most of us know as "the Internet" is actually a set of largely autonomous, loosely coordinated communication networks. As the influence of the Internet continues to grow, understanding its real nature is imperative to acting on a wide range of policy issues.
The Internet started out as research project of ARPA after World War 2. The goal was to design a network that could operate through a nuclear attack from the Soviets.
The top link is to a National Academies Press book “The Internet’s Coming of Age.” It explains basic design choices that underlie the Internet's success, identifies key trends in the evolution of the Internet, and evaluates current and prospective technical, operational, and management challenges, and explores the resulting implications for decision makers. Another resource is RFC 1958.

## Slide 36: Internet Architecture
Lecture 1
http://www.nap.edu/html/coming_of_age/
http://www.ietf.org/rfc/rfc1958.txt
Why did the Internet win?
  Packet switching over circuit switching
Notes: The reason the Internet has prevailed over the past few decades lies in several design decisions.
Packet switching was a huge departure from circuit switching that telephone networks traditionally used, and allowed them to build a network that was cheaper, faster, easier to scale and vastly more efficient and adaptable.

## Slide 37: Internet Architecture
Lecture 1
http://www.nap.edu/html/coming_of_age/
http://www.ietf.org/rfc/rfc1958.txt
Why did the Internet win?
  Packet switching over circuit switching
  End-to-end architecture and “Hourglass” design
Notes: The placement of network functionality was guided by a principle called the end-to-end principle. Most network functionality (like network applications and many network services) were placed at the network edge. The network core just moves the packets around and lets the recipient devices at the network edge figure out what to do.

## Slide 38: Internet Architecture
Lecture 1
http://www.nap.edu/html/coming_of_age/
http://www.ietf.org/rfc/rfc1958.txt
Why did the Internet win?
  Packet switching over circuit switching
  End-to-end architecture and “Hourglass” design
  Layering of functionality
Notes: The network functions are broken down and implemented in layers that makes it easy to plug and reuse network services across applications, as well as extend services and applications to new physical technologies.

## Slide 39: Internet Architecture
Lecture 1
http://www.nap.edu/html/coming_of_age/
http://www.ietf.org/rfc/rfc1958.txt
Why did the Internet win?
  Packet switching over circuit switching
  End-to-end architecture and “Hourglass” design
  Layering of functionality
  Distributed design, decentralized control
Notes: 4) When functions are widely distributed, breaking one part of the network does not cause the entire network to crash. The lack of a central authority is the key to why the Internet works, especially at times of unexpected demand.

## Slide 40: Internet Architecture
Lecture 1
http://www.nap.edu/html/coming_of_age/
http://www.ietf.org/rfc/rfc1958.txt
Why did the Internet win?
  Packet switching over circuit switching
  End-to-end architecture and “Hourglass” design
  Layering of functionality
  Distributed design, decentralized control
  Superior organizational process
Notes: 5) The last, but not the least important reason, is that the pioneers of the Internet also created an incredibly democratic, hacker-and results-oriented social structure that can update and upgrade the physical structure. Which is both a marvelous piece of engineering and foresight.

## Slide 41: Packet vs. circuit switching
Lecture 1
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 42: Case study: Circuit Switching
Lecture 1
1890-current: Phone network
  Fixed bit rate
  Mostly voice
  Not fault-tolerant
  Components extremely reliable
  Global application-level knowledge throughout network

## Slide 43: Case study: Packet Switching
Lecture 1
1981-current: Internet network
  Variable bit rate
  Mostly data
  Fault-tolerant
  Components not extremely reliable (versus phone components)
  Distributed control and management

## Slide 44: Circuit Switching
Lecture 1
End-end resources reserved for “call”
network resources (e.g., bandwidth) divided into “pieces”
  link bandwidth, switch capacity
  pieces allocated to calls
  resource piece idle if not used by owning call
    dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup and admission control required

## Slide 45: Circuit Switching: FDM and TDM
Lecture 1
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 46: Numerical example
Lecture 1
How long does it take to send a file of 640,000 bits from host A to host B over a circuit-switched network?
  All links are 1.536 Mbps
  Each link uses TDM with 24 slots/sec
  500 msec to establish end-to-end circuit
Let’s work it out!

## Slide 47: Network Core: Packet Switching
Lecture 1
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 48: Packet Switching: Statistical Multiplexing
Lecture 1
Sequence of A & B packets does not have fixed pattern, shared on demand statistical multiplexing.
TDM: each host gets same slot in revolving TDM frame.
A
B
C
10 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 49: Packet switching versus circuit switching
Lecture 1
N users over 1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
  Allows more users to use network
  “Statistical multiplexing gain”
Packet switching allows more users to use network!
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 50: Packet switching versus circuit switching
Lecture 1
Great for bursty data
  resource sharing
  simpler, no call setup
Bad for applications with hard resource requirements
  Excessive congestion: packet delay and loss
  Need protocols for reliable data transfer, congestion control
  Applications must be written to handle congestion
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
  Common practice: over-provision
Is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?

## Slide 51: How do loss and delay occur?
Lecture 1
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
when packet arrives to full queue, packet is dropped (aka lost)
  lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 52: Four sources of packet delay
Lecture 1
1. nodal processing:
  check bit errors
  determine output link
A
B
nodal
processing

## Slide 53: Four sources of packet delay
Lecture 1
1. nodal processing:
  check bit errors
  determine output link
A
B
nodal
processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 54: Delay in packet-switched networks
Lecture 1
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
A
B
transmission
nodal
processing
queueing

## Slide 55: Delay in packet-switched networks
Lecture 1
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 56: Nodal delay
Lecture 1
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 57: Queueing delay (revisited)
Lecture 1
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 58: Transmission delay
Lecture 1
Packet switching
  Store-and-forward
  Packet completely received before being transmitted to next node
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L
more on delay shortly …

## Slide 59: “Real” Internet delays and routes
Lecture 1
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 60: “Real” Internet delays and routes
Lecture 1
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link

## Slide 61: End-to-end principle and Hourglass design
Lecture 1

## Slide 62: End-to-end principle
Lecture 1
J. H. Saltzer, D. P. Reed and D. D. Clark “End-to-end arguments in system design”, Transactions on Computer Systems, Vol. 2, No. 4, 1984
http://www.acm.org/pubs/citations/journals/tocs/1984-2-4/p277-saltzer/
Notes: The most influential paper about placing functionality is “End-to-End Arguments in System Design” by Saltzer, Reed, and Clark.The “Sacred Text” of the Internet. There are endless disputes about what it means, everyone cites it as supporting their position.

## Slide 63: Hourglass design
Lecture 1
D. Clark, “The design philosophy of the DARPA Internet”, SIGCOMM 1988, August 16 - 18, 1988. http://www.acm.org/pubs/citations/proceedings/comm/52324/p106-clark/
Notes: David Clark talks beautifully about the design philosophy of the DARPA protocols and how it led to the hourglass design in this paper.
1. Connect existing networks
2. Robust in face of failures (not nuclear war...)
3. Support multiple types of services
4. Accommodate a variety of networks
5. Allow distributed management
6. Easy host attachment
7. Cost effective
8. Allow resource accountability

## Slide 64: End-to-end principle
Lecture 1
Where to put the functionality?
  In the network? At the edges?
End-to-end functions best handled by end-to-end protocols
  Network provides basic service: data transport
  Intelligence and applications located in or close to devices at the edge
  Violate principle as a performance enhancement
Leads to innovation at the edges
  Phone network: dumb edge devices, intelligent network
  Internet: dumb network, intelligent edge devices
Notes: A basic observation:
Some applications have end-to-end performance requirements
- reliability, security, etc.
Implementing these in the network is very hard: - every step along the way must be fail-proof
The hosts at the network edge:
can satisfy the requirement without the network - can’t depend on the network
What the end-to-end principle states: The function in question can completely and correctly be implemented only with the knowledge and help of the application standing at the end points of the communication system. Therefore, providing that questioned function as a feature of the communication system itself is not possible. (Sometimes an incomplete version of the function provided by the communication system may be useful as a performance enhancement.)

## Slide 65: Hourglass design
Lecture 1
End-to-end principle leads to “Hourglass” design of protocols
Only one protocol at the Internet level
  Minimal required elements at narrowest point
IP – Internet Protocol
  http://www.rfc-editor.org/rfc/rfc791.txt
  http://www.rfc-editor.org/rfc/rfc1812.txt
  Unreliable datagram service
  Addressing and connectionless connectivity
  Fragmentation and assembly
Notes: A single Internet layer module:
Allows all networks to interoperate
- all networks technologies that support IP can exchange packets
Allows all applications to function on all networks - all applications that can run on IP can use any network
Simultaneous developments above and below IP

## Slide 66: Hourglass design
Lecture 1
Simplicity allowed fast deployment of multi-vendor, multi-provider public network
  Ease of implementation
  Limited hardware requirements (important in 1970s)
    Is it relevant now with today’s semiconductor speeds?
  Eventual economies of scale
Designed independently of hardware
  Hardware addresses decoupled from IP addresses
  IP header contains no data/physical link specific information
  Allows IP to run over any fabric
Notes: Each network is independent and must not be required to change. Then ARPANET, X.25, DARPA Satellite Network.
Best-effort communication
Boxes (routers) connect networks No global control at operations level.

## Slide 67: Hourglass design
Lecture 1
Waist expands at transport layer
Two dominant services layered above IP
TCP – Transmission Control Protocol
  Connection-oriented service
  http://www.rfc-editor.org/rfc/rfc793.txt
UDP – User Datagram Protocol
  Connectionless service
  http://www.rfc-editor.org/rfc/rfc768.txt

## Slide 68: Hourglass design
Lecture 1
TCP – Transmission Control Protocol
  Reliable, in-order byte-stream data transfer
    Acknowledgements and retransmissions
  Flow control
    Sender won’t overwhelm receiver
  Congestion control
    Senders won’t overwhelm network

## Slide 69: Hourglass design
Lecture 1
UDP – User Datagram Protocol
  Unreliable data transfer
  No flow control
  No congestion control
Notes: Realized TCP wasn’t needed (or wanted) by some applications
Separated TCP from IP, and introduced UDP - What’smissingfromUDP?

## Slide 70: Hourglass design
Lecture 1
What uses TCP?
  HTTP, FTP, Telnet, SMTP, NNTP, BGP, IMAP, POP
What uses (mainly) UDP?
  SNMP, NTP, NFS, RTP (streaming media, IP telephony, teleconferencing), multicast applications
  Many protocols can use both
Check out /etc/services on *nix or C:\WIN*\system32\services
IANA
  http://www.iana.org/assignments/port-numbers

## Slide 71: Hourglass design
Lecture 1
Security?
Quality-of-service?
Reliable, out-of-order delivery service?
Handling greedy sources?
Accounting and pricing support?
IPsec, DiffServ, SCTP, ….

## Slide 72: Hourglass design
Lecture 1
Security?
Quality-of-service?
Reliable, out-of-order delivery service?
Handling greedy sources?
Accounting and pricing support?
IPsec, DiffServ, SCTP, ….

## Slide 73: End-to-end principle and the Hourglass design
Lecture 1
The good
  Basic network functionality allowed for extremely quick adoption and deployment using simple devices
The bad
  New network features and functionality are impossible to deploy, requiring widespread adoption within the network
  IP Multicast, QoS
Notes: The benefit of the end-to-end principle is that it allowed for very quick deployment of new devices, applications and services, which in turn attracts new users to the Internet and helps the network grow.
The growth of the network in turn unleashes the development of new applications, which require richer network functionality.
The downside of the end-to-end principle is that it is nearly impossible to deploy richer new features that require routers or the network core to deploy new code. IP Multicast and QoS were two features that were proposed as extensions to IP, and proved impossible to deploy for well over a decade after they were proposed.

## Slide 74: This Lecture
We learned how to share the infrastructure across many connections/flows
We also learned about the implications of the sharing scheme (circuit switching or packet switching) on the service that the traffic receives
Notes: To summarize, two key ideas that we learned in this course were how to share the infrastructure across many connections/flows and the implications of the sharing scheme on the service that the traffic receives.

## Slide 75: Next Steps
Read for the next lecture
  “The Design Philosophy of the DARPA Internet Protocols”
  Kurose & Ross, Chapter 1, Sections 1.1-1.3.
    Can skim through discussion on access networks and physical media.
Lecture 1
Notes: I am listing readings for the next lecture. Skimming through them will help clarify details about the ideas I have discussed.

## Slide 76: Acknowledgements
Lecture 1
A few slides in this lecture have been adapted from:
  Kurose/Ross
  Srini Seshan’s networking course