## Slide 1: Lecture 3: Internetworking Protocols
Part 1: Introduction
Part 2: Application Layer

## Slide 2: Layering
Modular approach to network functionality
  Simplifies complex systems
  Each layer relies on services from layer below and exports services to layer above
  Hides implementation, eases maintenance and updating of system
    Layer implementations can change without disturbing other layers (black box)

## Slide 3: Layering
Examples:
  Topology and physical configuration hidden by network-layer routing
    Applications require no knowledge of this
    New applications deployed without coordination with network operators or operating system vendors
Link hardware
Host-to-host connectivity
Application

## Slide 4: Layering in Protocols
Set of rules governing communication between network elements (applications, hosts, routers)
Protocols specify:
  Interface to higher layers (API)
  Interface to peer
    Format and order of messages
    Actions taken on receipt of a message
  Interface defines interaction
Notes: Human analogy – social customs

## Slide 5: Layering in Networks: OSI Model
Physical
  how to transmit bits
Data link
  how to transmit frames
Network
  how to route packets host-to-host
Transport
  how to send packets end2end
Session
  how to tie flows together
Presentation
  byte ordering, formatting
Application: everything else
Host
Application
Transport
Network
Data Link
Presentation
Session
Physical

## Slide 6: Encapsulation
message
segment
datagram
frame
source
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
Hl
M
Ht
Hn
Hl
M
router
switch

## Slide 7: Distributed design and control
Requirements from DARPA
  Must survive a nuclear attack
Reliability
  Intelligent aggregation of unreliable components
  Alternate paths, adaptivity
  Distributed management & control of networks
Exceptions: TLDs and TLD servers, IP address allocation (ICANN)
Back

## Slide 8: Superior organizational process
IAB/IETF process allowed for quick specification, implementation, and deployment of new standards
  Free and easy download of standards
  Rough consensus and running code
  2 interoperable implementations
  Bake-offs
  http://www.ietf.org/
ISO/OSI
  Comparison to IETF left as an exercise
Back

## Slide 9: A day in the life of an Internet host…
Booting
  Dynamically configure network settings
    DHCP, BOOTP request
      UDP (unreliable datagrams)
      IP and data-link broadcast
    DHCP, BOOTP response from listening server
      IP address of host, DNS server, and default router
      Netmask (i.e. 255.255.255.0) to determine network ID

## Slide 10: A day in the life of an Internet host…
Web request http://www.yahoo.com/index.html
  Step #1: Locate DNS server
    if (netmask & IPHost == netmask & IPDNS)
      DNS server on local network
      ARP for hardware address of IPDNS
    else
      DNS server on remote network
      ARP for hardware address of IPDefaultRouter
    ARP (Address Resolution Protocol)
      IP address to hardware address mapping
      Request broadcast for all hosts on network to see
      Reply broadcast for all hosts to cache

## Slide 11: A day in the life of an Internet host…
Step #2: ARP request and reply

## Slide 12: A day in the life of an Internet host…
Step #2: DNS request and reply
  UDP, IP, data-link header
Datalink header
(host)
IP of host
UDP Header
DNS reply
www.yahoo.com
is 216.115.105.2

## Slide 13: A day in the life of an Internet host…
Step #3: TCP connection establishment + HTTP request and reply
    HTTP (application data) “GET index.html” “HTTP/1.0”
    TCP (session establishment, reliable byte stream)
    IP, data-link header
Datalink header
(host)
IP of host
TCP Header
HTTP reply
HTTP/1.0 200 OK
Date: Mon, 24 Sep 2001
Content
-
Type: text/html
<HTML>
etc…

## Slide 14: A day in the life of an Internet host…
Role of TCP and UDP?
Demultiplex at end hosts.
  Which process gets this request?
FTP
HTTP
TFTP
NV
TCP
UDP
IP
NET1
NET2
NETn
…
TCP/UDP
IP
IPX
Port Number
Network
Protocol Field
Type Field

## Slide 15: A day in the life of an Internet host….
What about….
  Reliability
    Corruption
    Lost packets
  Flow and congestion control
  Fragmentation
  Out-of-order delivery
The beauty of TCP, IP, and layering
  All taken care of transparently

## Slide 16: What if the Data gets Corrupted?
Internet
GET windex.html
GET index.html
Solution: Add a checksum
Problem: Data Corruption
0,9
9
6,7,8
21
4,5
7
1,2,3
6
X

## Slide 17: What if the Data gets Lost?
Internet
GET index.html
Problem: Lost Data
Internet
GET index.html
Solution: Timeout and Retransmit
GET index.html
GET index.html

## Slide 18: What if receiver has no resources (flow control)?
Internet
PUT remix.mp3
Problem: Overflowing receiver buffers
Internet
Solution: Receiver advertised window
PUT remix.mp3
16KB free

## Slide 19: What if Network is Overloaded?
Short bursts: buffer
What if buffer overflows?
  Packets dropped and retransmitted
  Sender adjusts rate until load = resources
Called “Congestion control”

## Slide 20: What if the Data Doesn’t Fit?
Problem: Packet size
Solution: Fragment data across packets
On Ethernet, max IP packet is 1.5kbytes
Typical web page is 10kbytes
GET
inde
x.ht
ml
GET index.html

## Slide 21: What if the Data is Out of Order?
Solution: Add Sequence Numbers
Problem: Out of Order
GET
x.th
inde
ml
GET x.thindeml
GET index.html
ml
4
inde
2
x.th
3
GET
1

## Slide 22: The rest of the course
From birds-eye view, we will now focus on specific components
Review these lectures for perspective when looking at the components
Mostly classical material with some references to newer technologies